## Slide 1: The LHC long term upgrade plans and the CERN Magnet development program Gijs de Rijk CERN

## Slide 2: Content
LHC performance and short term plans
The long term upgrade plans for the LHC
Accelerator R&D magnet programs for the upgrades

## Slide 3: The 2011 LHC run
p-p 5 fb-1
Pb-Pb 150 mb-1

## Slide 4: The 2012 LHC plan/prediction
Energy 4 TeV per beam, Integrated Luminosity 16 fb-1
Decisions after Chamonix12 meeting
Lower b* (down to 0.6 m)
Tight collimator settings
50 ns bunch spacing
Pileup ≤30 events per crossing
Many (small) HW and operation modifications
  R2E mitigation
  Fast turnaround
  Improved procedures

## Slide 5: 2012: What is the envisaged maximum beam energy?
The issue is the stability of the 13kA splices between the main magnet bus-bars
If during 2012 the number of high current quenches stays below 5-6 then we have the same probability of burn-out as during 3.5 TeV run in 2011 with 40 quench limit (and we had 0 in 2011)
1 quench/month
No show-stoppers from equipment point of view to operate LHC in 2012 at maximum beam energy of up to 4 TeV

## Slide 6: LHC and the nominal performance
Nominal performance: 7 TeV per beam, Lpeak 1. 1034 cm-2s-1,
(25 ns bunch spacing; 2808 bunches; 1.15 1011 protons p bunch; b* 0.55 m;
Transverse norm. emittance 3.75 mmrad; bunch length 7.55 cm, 19 events/crossing)
What’s still less ?
Energy: 2011 3.5 TeV ; 2012 4 TeV
  Splice stability risk: to be fixed in 2013-2014 shutdown LS1
  Dipole training memory loss: training up to 6.5 TeV in 2014, the step to 7 TeV is then to be seen later
Bunch spacing: 50 ns at the moment (1400 bunches): scrubbing runs needed to overcome e- cloud formation (only tests in 2012)
What’s already more ?
Bunch intensity 1.5 1011 protons p bunch
Transverse norm. emittance 2.5 mmrad

## Slide 7: Schematic LHC layout

## Slide 8: LHC nominal parameters
Circumference 26.7 km
Beam energy at collision 7 TeV
Beam energy at injection 0.45 TeV
Dipole field at 7 TeV 8.33 T
Luminosity 1034 cm-2.s-1
Beam current 0.56 A
Protons per bunch 1.1x1011
Number of bunches 2808
Nominal bunch spacing 24.95 ns
Normalized emittance 3.75 mm
Total crossing angle 300 mrad
Energy loss per turn 6.7 keV
Critical synchrotron energy 44.1 eV
Radiated power per beam 3.8 kW
Stored energy per beam 350 MJ
Stored energy in magnets 11 GJ
Operating temperature 1.9 K

## Slide 9: Looking towards an interaction point

## Slide 10: LHC planning and forecast for the next 10 years
LS3

## Slide 11: time line of CERN LHC tunnel (proto) projects
1980
1990
2000
2010
2020
2030
LEP
Constr.
Physics
Upgr.
LHC
Constr.
Physics
Proto.
Design,
R&D
HL-LHC
Constr.
Physics
Design,
R&D
LHeC
Constr.
Physics
Design,
R&D
HE-LHC
Constr.
Physics
Design,
R&D
Source: L. Rossi. LMC 2011 (modified)
  runs in parallel to HL-LHC; tight R&D schedule
  follows HL-LHC; R&D & protot. time < for LHC
2040

## Slide 12: HL-LHC
HL-LHC Final Goal: Given by Physics: 3000 fb-1 in 10-12 years of running

## Slide 13: HI-LUMI for HL-LHC: The HL composition
Collimation
Project
Matching section and correctors
Beam Diagnostics
High Field Magnets R&D
HE-LHC Studies
Hardware Commissioning

## Slide 14: LHC planning and forecast for the next 10 years
LS3

## Slide 15: LS1: go to the full energy
Consolidation of the splices (soldering connections between the magnets):
Replace magnets with an issue
Repair known issues
Total magnet to magnet interconnects in the machine: 1 695
Total 13 kA splices: 10 170
Number of splices to be redone: ~1 500 (15%)
Number of shunts to be applied: > 27 000

## Slide 16: LS1 Splice intervention train
Start at P5 / clockwise
5
1
8
2
3
4
7
6
High inner splice
SSS
Highest leak
Electrical integrity issue
Beam optics
Spread all around : work on leaks, PIMs,
SAM (He, DN160)
Y-lines repair
CC Consolidation / Inspection
DN 200 installation
Triplet braid (End of LS1 for rad prot)
Cryo-dipole
Circuit and splices issues
Critical reversed beam screen

## Slide 17: Global Planning LS1
Preliminary powering tests
Warm-up
Opening
Splice consolidation
(incl. internal leak tests)
Closure
Leak tests (Ins vacuum)
Preparation for cool-down
Cool-down
ELQA@cold
Powering tests

## Slide 18: LHC planning and forecast for the next 10 years
LS3

## Slide 19: LS2: first steps of HL-LHC
Shut down to overcome some beam intensity limitations
  Collimation of off momentum particles in the Dispersion suppressors: replace 15 m 8T dipole with a 11 m 11T dipole to gain space for the collimator
  New Cryo P4
  Injectors Upgrade

## Slide 20: LHC planning and forecast for the next 10 years
LS3

## Slide 21: After LS3: Machine cycling for HL-LHC
20E+34
pile up
heat deposition in IR and DS
other?
Levelling
150 days of Physics /y of this cycle
with 60% efficiency will give 250 fb-1/y
The set of parameters we need to reach this goal: the scenarios are known

## Slide 22: LS3: full implementation of HL-LHC
Many changes : IR Magnets (triplet, D1, D2, MQ4, …), SC Crab Cavities, IR Col, New Cryo IP1-IP5, Cold Powering on surface 0.1-1 GW d.c. HT

## Slide 23: What is needed for L= 5 .1034 cm-2s-1 ? (1)
  High Gradient/Large Aperture insertion Quadupole magnets
    Possibly: l = 8 m, G= 150 T/m, A=140 mm, (Bpeak-ss =13 T)
     ≤ 22 cm are possible with a factor 2.5 in luminosity by itself,
    Necessarily coupled with a mechanism to compensate the geometrical reduction .
  Crab Cavities:
    best candidate for exploiting small  (for nominal only +15%).
    However today Crab Cavities are not validated for LHC , conceptually the desin is moving fast: the issue of machine protection should be addressed with priority.
    Global Scheme: 1 cavity in IP4, Proof on LHC, good for 1 X-ing.
    Local scheme; 1 cavity per IP side

## Slide 24: What could be needed for L= 5 .1034 cm-2s-1 ? (2)
  Separation dipole D1: 8 T , 3.5 m long , 150 mm aperture
  SC links to replace at the surface electronic equipment today in the tunnel and exposed to high radiation (Power Converters & DFBs)
  New Cryoplants in IP1 & IP5
  Improve some correctors
  Commissioning the lattice sextupoles @ 600-650 A
  New MQT corrector scheme using existing spare 600 A bus bars
  Review Matching section (MS) : new large aperture Q4 (today 2x70 mm)
  Matching section : with new stronger corrector orbit, displacements of few magnets
  Larger aperture separation magnet D2
  Cryo-plant for RF in point 4 : 5-7 kW @ 4.5 K
  For extra collimators: l = 11 m, B= 11 T Dispersion Supressor dipoles

## Slide 25: Crab Cavities
When colliding under an collision angle, if the beams are not ‘head on’ there is a geometrical reduction factor in the luminosity.
Cure: turn the bunches with a transversely accelerating RF field
First successfully used at KEK B-factory BELLE
qc

## Slide 26: Crab Cavities
Elliptical 800 MHz is not far from being designed. Requires a 400 mm beam-beam distance
400 MHz small cavity under conceptual study, they can (?) fit in 194 mm beam-beam. Required for final solution
Work done by the LARP collaboration, EuCARD and at CERN
Ref. : F. Zimmermann, Ed Ciapala

## Slide 27: Crab Cavities: fast progress since 2 years
They started building crab cavities in Europe and the US!

## Slide 28: SC link to remove Power Convertors from High Rad zones
Semi-horizontal link (100-700 m)
Vertical link
H = 100 m
1.1 mm
MgB2 wire
Courtesy: A. Ballerino

## Slide 29: HE-LHC – (33 TeV cms)
2-GeV Booster
Linac4
SPS+,
1.3 TeV, 2030?
HE-LHC
2030?
By courtesy of our DG

## Slide 30: CERN program on High Field Magnets
HFM program aim: High field magnets technology (dipoles and quads) for LHC upgrades and future accelerators
Priorities: - Conductor is the heart of the magnet
        - Magnet design and tests
        - Germinate new projects
First step (2004 – 2012):
    Conductor technology : NED 1.25 mm, Fresca2 1 mm (2010), 11 T 0.7 mm (2011)
    Magnet technology : Short Model Coil (2011)
    Personnel training on existing technologies : test TQ & HQ @ CERN (2009)
Second step (2009 – 2014):
    Magnet models : Fresca2 (2013), IR quad model (2013), 11 T dipole model (2013)
    Conductor test facilities upgrade to 15 T test station (2014-2015)
    Radiation hardness studies for Nb3Sn and coil insulation (2010-2014)
    Magnet concepts from 15 T to 20 T : EuCARD 6 T insert (2013), EuCARD2 (2016)
Third step (2014 – 2016):
    LHC Dispersion Suppressor dipole prototype (2015)
    LHC Inner triplet quadrupole prototype (2016)

## Slide 31: HFM program gantt chart
Continuous conductor development , starting with Nb3Sn , now also HTS
From the HFM project new construction projects germinate
After 2016 this will result in : IT Quad construction, 11 T DS construction and a more targeted HE-LHC magnet development project

## Slide 32: Conductors for HFMs
To meet these requirements one has to switch from Nb-Ti to Nb3Sn conductors
Engineering current density in practical superconductors
Courtesy E. Todesco

## Slide 33: Superconductors
Compilation of engineering current densities

## Slide 34: Conductor R&D - NED and post-NED strands
The NED program (2004-2008/2010) achieved Nb3Sn 1.25 mm strands with JC of 1500 A/mm2 at 15 T and 4.2 K, filament diameter of 50 m, and RRR regularly in excess of 150
The HFM program has since focussed on issues of cable production and degradation, and thermo-magnetic stability
Bruker-EAS PIT, 288 subelements, (Nb-Ta)3Sn
Courtesy L. Bottura, B. Bordini

## Slide 35: Conductor R&D: improve Jc and stability
Courtesy of B. Bordini (CERN)
Conductors to be studied in detail:
Nb3Sn Critical current as function of field and temperature
Nb3Sn stability: magneto-thermal instabilities understanding
Accompany industry with detailed characterization and metallurgic studies
Example:
Magneto-thermal instabilities
In-depth study to understand this effect which was seen in other labs,
Guide strand choice and strand layout development :
-small sub-elements ≤50 μm
-reduce strand diameter: 1mm, -high RRR: ≥100
-reduce Jc: 1250A/mm2@15T, 4.2 K

## Slide 36: Cables for HFM Program
SMC Dipole cable – 14 strands (1.25 mm) and
18 Strands (1 mm), Width = 10 mm, Twist Pitch = 60 mm
Average IC degradation 0 … 4 %
DS Dipole cable – 40 Strands (0.7 mm)
Width = 14.7 … 15.1 mm, Twist Pitch = 100 mm, 0.8° keystone
Average IC degradation < 3 %
Fresca 2 Dipole cable – 40 Strands (1 mm)
Width = 20.9 mm, Twist Pitch = 120 … 140 mm
Average IC degradation < 15 %
Cabling by L. Oberli and A. Bonasia (CERN)
Cabling tests were performed on several variants of strands/cable sizes to explore the space of parameters, and among others: dimensions, compaction, twist pitch, cabling angle and cabling force, …
Cabling degradation was reduced from 45 % (worst case) to negligible (within the scatter of measurements of extracted strands)

## Slide 37: A high current HTS (YBCO) cable
Roebel cables of punched HTS tapes after an idea of W. Goldacker (KIT)
Manufacturing by IRL Ltd.
First test at liquid helium (4.3 K) and in high field (10 T) show a current carrying capacity of 4 to 10 kA
By courtesy of J. Fleiter, Ph. Denis, G. Peiro, A. Ballarino

## Slide 38: High Field Magnet R&D
HQ/LHQ
Nb3Sn Quadrupole
US-LARP program
Short Model Coil
FReSCa2
Nb3Sn Dipole
Race-track
Model Coil
11 T DS
Nb3Sn Dipole
11 T DS
1-in-1 model
2012
2013
2014
2015
2016
2017
2018
2019
2020

## Slide 39: EuCARD WP7 High Field Magnets
12 partner collaboration : CEA-Saclay, CERN, CNRS-Grenoble, Columbus (Genova), BHTS (Bruker), INFN-LASA (Milano), KIT (Karlsruhe), PWR (Wroclaw), SOTON (Southampton), STFC-Daresbury, TUT (Tampere), UNIGE (Genève)
One management and 5 R&D tasks:
Coordination and Communication.
Support studies, thermal studies and insulation radiation hardness
High field model: 13 T, 100 mm bore (Nb3Sn)
Very high field dipole insert (in HTS, up to ΔB=6 T)
High Tc superconducting link (HTS powering links for the LHC)
Short period helical superconducting undulator (ILC e+ source)
Duration: 1-4-2009 – 31-3-2013, Budget:6.4 M€ total, 2.0 M€ EC contr.
  40 mm
25 × 2 × 600 A

## Slide 40: SMC, tested in 2011: 12.5 T on the coil
Courtesy of J. Perez and M. Bajko

## Slide 41: EuCARD High field model (Fresca2)
Diameter Aperture = 100 mm
L coils = 1.5 m
L straight section = 700 mm
L yoke = 1.6 m
Diameter magnet = 1.03 m
156 turns per pole
Iron post
Bcenter = 13.0 T
I13T = 10.7 kA
Bpeak = 13.2 T
Emag = 3.6 MJ/m
L = 47mH/m
Courtesy Attilio Milanese, Pierre Manil
42
42
36
36
Challenging construction with several new concepts:
Block coil geometry with flared ends
Shell-bladder and key structure
(inspired by the HD2 of LBNL)
Construction ongoing, first coil 2012, test end 2013

## Slide 42: Dispersion Suppressor Upgrade: collimators & 11 T dipoles
11 T Nb3Sn
LS2 2017-18: Point-3,7 & IR-2
LS3 2020+: IR1,5 as part of HL-LHC
MB.B8R/L
MB.B11R/L
5.5 m Nb3Sn
5.5 m Nb3Sn
3 m Collim.
5.5 m Nb3Sn
5.5 m Nb3Sn
3 m Collim
11 m Nb3Sn
3 m Collim
LS2: 12 coldmass + 2 spares = 14 CM
LS3: 8 coldmass + 2 spares = 10 CM
Total 24 CM
LS2: 24 coldmass + 4 spares = 28 CM
LS3: 16 coldmass + 4 spares = 20 CM
Total 48 CM
∫BdL = 119.2 Tm @ Inom = 11.85 kA
in series with MB with 20 % margin

## Slide 43: HFM R&D for an LHC luminosity upgrade: 11T DS dipole
  Development started for a twin aperture Æ = 60 mm, B = 11 T, L = 5.5 m dipole magnet:
  40 strands of 0.7 mm
  2 layers 14.7 mm width cable
  B=11.0 T at 80.4% Iss, T=1.9 K, I=11850 A
  Coil length 5.3 m
  Issues being addressed:
  Stability of the strand at 1.9 K
  LHC dipole like collar structure
  Insulation type
  Heat removal from the coil
  Inter-strand resistance in the cable : cored cable
  Is sub-element diameter 50 mm small enough ? 30 mm

## Slide 44: 11T Dispersion Suppressor dipole
Courtesy M. Karppinen,
A. Zlobin, et al.
Developed at FNAL and CERN for the LHC luminosity upgrade.
two 5.5 m 11 T dipoles should replace one 15 m 8.3 T main dipole
Has to operate in series with the main bend dipole chain: 11 T @ 11850 A
Potentially the first Nb3Sn magnet to be used in an accelerator (2017)

## Slide 45: HFM R&D for an LHC luminosity upgrade: IT Quad
R&D in the US (LARP):
Up to now achieved (LQ): Aperture Æ = 90 mm, G = 220 T/m, L = 3.4 m
Now testing (HQ): Aperture Æ = 120 mm, G = 170 T/m, L = 1 m
Conductors used:
OST-RRP-54/61 and OST-RRP-108/127
Cable 27 strands, Æ = 0.7 mm , sub-elements Æ = 50 mm
Issues to address:
Inter-strand resistance in the cable is low and variable : used a core in the cable
Stability of the strand at 1.9 K to be confirmed
In the sub-element diameter of 50 mm small enough ? : develop 30 mm
Length limit at 3.4 m, should be 8 m
Radiation hard insulation
Heat removal from the coil

## Slide 46: LARP IT quad development program
Achieved with Nb3Sn:
TQ: 1 m, 220 T/m, 90 mm aperture
LQ: 3.8 m, 220 T/m, 90 mm aperture
HQ: 1 m, 170 T/m, 120 mm aperture
with alignment features
Plan:
4 m LHQ technology demonstrator by 2015

## Slide 47: HTS inserts
EuCARD
  6 T insert built with YBCO tapes
  Current density of 250 A/mm2
  Race-track, 20 mm aperture (no bore) self-supported for test in FReSCa-2
EuCARD2 (proposed)
  5 T, 40 mm bore, accelerator quality HTS magnet
  10 kA-class HTS cable at 20 T
5 T cos-q magnet design based on flat cable geometry
By courtesy of B. Auchmann

## Slide 48: EuCARD, 6 T insert (2009-2013)
Conductor: YBCO 12 mm tape, back to back soldered, and 2 in parallel, transposed between the poles
Number of turns 73 + 61 + 36 = 170 (of 4 tapes)
Aperture h = 20 mm , w = 15 mm “chopped cylinder” inside racetrack
Force detainment with welded clamp + shrinking rings
L total = 700 mm
L straight part = 274 mm
I = 2800 A
Detailed insert design ongoing
Manufacturing of test solenoid pancakes in progress
Test of test solenoids this year
Quench studies in progress
3D geometry
350 mm
700 mm
Courtesy:
J-M Rey (CEA),
P. Tixador (CNRS & Grenoble)
A. Ballarino (CERN)

## Slide 49: A really high field dipole
HTS/Nb3Sn/Nb-Ti nested coil magnet
low-grade
Nb3Sn
high-grade
Nb3Sn
HTS
Nb-Ti
By courtesy of E. Todesco
Bcoil
Nb-Ti
Nb3Sn
HTS
x 2
x 3

## Slide 50: Radiation resistance
The radiation resistance of the Nb3Sn magnets (and HTS) has to be fully proven
  Effects of radiation on the superconductor, the stabiliser (Cu, Al) and the insulator
CERN started in 2010 a program to test radiation effects on the Nb3Sn conductor
  Radiation tests on Nb3Sn conductor carried out at ATI (Vienna) and Kurchatov (Russia)
In the EUCARD program there is a task to select radiation hard insulator material material (impregnation) for the Nb3Sn coils
  Radiation tests on Nb3Sn insulation carried out in at Swierk (Poland) (irradiation starting this month)

## Slide 51: Radiation resistance: irradiation tests
Insulator electron irradiation at Swierk
Courtesy M. Chorowski (PWR)
Courtesy H. Weber (ATI)
Measurement of Jc of various HEP-grade Nb3Sn strand in the TRIGA reactor at the Atominsitut of the Technical University in Vienna

## Slide 52: Spare slides

## Slide 53: 2012 parameter table (protons)
Parameter | Value at 450 GeV | Value at top energy
Energy [ GeV ] | 450 | 4000
β*IP1/5 [ m ] | 11.0 | 0.6
β*IP2 [ m ] | 10.0 | 3.0
β*IP8 [ m ] | 10.0 | 3.0
Parallel separation [ mm ] | 2.0 | 0.67
Crossing angle IP1/5 [ μrad ] | 170 | 145
Crossing angle IP2 [ μrad ] | 170 | 90+
Crossing angle IP8 [ μrad ] | 170 (H) | 100 (V)
Ramp duration [ s ] | 2010: 1020 → 770 | 
Squeeze duration [ s ] | 2010: 548 (1.0 m) → 819 (0.6 m) | 
Collision BP duration [ s ] | 2010: 56 → 56 | 

## Slide 54: Top energy - IV
Comparison of performance reach for various options at 4 TeV (again focusing on ATLAS and CMS).
Parameter | Unit | 50 ns |  |  | 25 ns
Half crossing angle IP1/5 | mrad | 118.00 | 134.00 | 145.00 | 192.00
Beta * IP1/5 | m | 0.90 | 0.70 | 0.60 | 0.80
Total number of bunches |  | 1380 | 1380 | 1380 | 2760
Bunch intensity (1011) |  | 1.50 2.50 | 1.50 2.50 | 1.50 2.50 | 1.15 3.50
Normalised transverse emittance | mm |  |  |  | 
Protons per beam (1014) |  | 2.07 | 2.07 | 2.07 | 3.17
Current per beam | mA | 372.43 | 372.43 | 372.43 | 571.07
Stored energy per beam | MJ | 132.69 | 132.69 | 132.69 | 203.46
RMS bunch length | cm | 9.40 | 9.40 | 9.40 | 10.10
Beam size IP1/5 | mm | 0.023 | 0.020 | 0.019 | 0.026
Geometric factor IP1/5 |  | 0.901 | 0.849 | 0.809 | 0.797
Number of colliding pairs in IP1/5 |  | 1331 | 1331 | 1331 | 2662
Luminosity in IP1/5 (1033) | cm-2 s-1 | 4.57 | 5.54 | 6.16 | 3.82
Events per crossing IP1/5 (76 mbarn) |  | 23.22 | 28.15 | 31.29 | 10.0

## Slide 55: 2012 proton run – 50 ns
Assumptions:
  147 days of physics
  22 days of MDs
  21 days of commissioning with beam (small number of bunches)
  20 days of Technical stops
  6 (2x3) days of recovery after Technical Stops
  8 days of special physics runs
  3 day of scrubbing with 25 ns beam including setting-up and 1 day of contingency. To be planned as soon as possible before serious intensity ramp-up.
Intensity ramp up as discussed in Evian (for 50 ns):
  48-84-264-624: 3 fills and 6 hours of Stable Beams (assumed 25% SB time)
  840-1092-1380: 3 fills and 20 hours of Stable beams (assumed 28% SB time)
   2 weeks for validation of maximum number of bunches

## Slide 56: 50 ns – 4 TeV – very optimistic
HF=0.26
Nb ramp
L=0.75  0.9 Lpeak
HF=0.26
control
L=0.75  0.9 Lpeak
HF=0.26
Peak perf.

## Slide 57: 25 ns -4 TeV
HF=0.2
No experience with this beam!!!

## Slide 58: Summary table